M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme. For further information contact Interface’s Technical Department.

Net Effect B702 - Carpet Tiles

A tufted patterned structured loop pile manufactured from 100% recycled BCF solution dyed nylon, contains pre and post-consumer recycled content, with a Graphlex® backing.  Available in 8 colourways and carries a Class 33 heavy contract classification.  The 7.1mm thick tile is available in 250 x 1000mm size as standard. Size options are available with minimum quantities.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral.  Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: N/a. Carpet tiles to be adhered direct to the subfloor.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Net Effect – B702 Carpet Tiles

- Type: Tufted patterned structured loop pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC2

Size: 250 x 1000mm standard size. 
Colour/pattern: 312896 Black Sea / 312897 North Sea / 312898 Pacific / 312899 Arctic / 312900 Atlantic / 312901 Caspian / 312902 Sand / 312903 Driftwood

Method of laying: Herringbone, Ashlar

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com