M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme, using the Image range of cleaning materials. For further information contact Interface’s Technical Department.

# Equilibrium Carpet Tiles

A tufted patterned structured tip sheared pile tile manufactured from recycled solution dyed nylon with Graphlex® backing.

The range is available in 30 colourways and carries a Class 33 heavy contract classification. The 8.1mm thick tiles are available in 500 x 500mm as standard.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral. Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: Should be laid where required over existing timber bases.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Equilibrium Carpet Tiles

- Type: Tufted patterned structured tip sheared pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC2

Size: 500 x 500mm standard size

Colour/pattern: 304200 Balance/ 304201 Correlation/ 304202 Vitality / 304203 Simplicity/ 304204 Entity / 304205 Persistence / 304206 Analogy / 304207 Continuity / 304208 Consistency / 304209 Equality / 304210 Unity / 304211 Accuracy / 304212 Proportion / 304213 Similarity / 304214 Classification / 304215 Integrity / 304216 Arrangement / 304217 Ability / 304218 Coincidence / 304262 Constant/ 304271 Parity/ 304281 Mobility/ 304282 Fluctuation/ 304286 Equation/ 304287 Symmetry/ 304289 Serenity/ 304293 Contentment/ 304295 Harmony/ 304296 Moderation/ 304298 Uniformity

Method of laying: Monolithic, Quarter Turn and Ashlar.

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com